## Slide 1: Minimizing MNA Complexity
MNA Co-chairs

## Slide 2: MNA Complexity Concerns - I
There is a concern that the current MNA approaches too complicated.
MPLS Core design
Mapping of an opaque label to a previous agreed function.
The simple data-plane gives flexibility and ability to evolve the MPLS functionality without redesign of the packer parser.
Current MNA design
In-stack data and flags, is contrary to MPLS architecture. The risk is that it will rapidly ossify, and it will be expensive to add new functionality and hard to correct early design errors.
MPLS Fundamental Design
It is the design philosophy of MPLS not to use SPLs unless there was no alternative. This has stood the MPLS community in good stead for 25 years.

## Slide 3: MNA Complexity Concerns - II
HW capabilities
Most forwarders can do two label lookup - they need to do so for multicast
Most forwarders can find the bottom of stack and look past it.
A Proposed MNA approach
Consider an approach where a new forwarding FEC is introduced
  The FEC should have the property forward to given destination (same normal MPLS forwarding)
  It should also have the property of activating the feature vectored to by a label that follows (called a modifier).
Ancillary data
The structure of the ancillary data carried below bottom of stack is a function of modifier label - just as it is in other MPLS functions such as PW, Detnet, VPN etc.

## Slide 4: MNA Complexity Concerns - III
Tradition of MPLS
This approach is better suited to operator and vendor specified functions without limiting our ability to standardize the common functions.
Seeking WG Consensus
The advantages and disadvantages of returning to a model closer to “traditional” MPLS need to be analysed by the MPLS WG and a consensus decision taken.