## Slide 1: Choosing Streams
Andy Pepperell

## Slide 2: Basic message flow
Media Stream Consumer
Media Stream Provider
Consumer capability advertisement
Media capture advertisement
Consumer configuration
of provider’s streams
Notes: Consumer must send at least one capability advertisement near the start – provider should wait for this before sending an initial media capture message
Consumer able to send any number of further capability advertisements during the call – provider may respond to these with changed media capture advertisements
Provider able to send any number of media capture advertisements during the call, and consumer should respond appropriately – e.g. configuring (instantiating) more streams if needed, or de-configuring those currently configured that are no longer valid

## Slide 3: Capabilities Sent by Consumer
Media Stream Consumer
Consumer capability advertisement
Physical factors
User preferences
e.g. number of screens
Software limitations
e.g. media capture attributes known
Notes: Inputs / determining factors on the left, result on the right (capabilities message sent to provider)
Capabilities / hints as sent by the stream consumer to the provider likely to be determined by the hardware characteristics of the device and essentially which “version” of CLUE is known about (as exemplified by the media capture attributes communicated to the provider)

## Slide 4: Advertisement Sent by Provider
Media Stream Provider
Media capture advertisement
Consumer capability advertisement
Provider fixed characteristics
Dynamic factors
e.g. number of cameras
e.g. whether presentation source present
Notes: Media stream provider factors in consumer’s capabilities and its own fixed and dynamic characteristics to come up with the media capture advertisement to send to the media stream consumer
“Dynamic factors” part can change during the call, for instance due to a presentation source being activated / de-activated, at which point the media stream provider should re-advertise

## Slide 5: Configure Msg Sent by Consumer
Media Stream Consumer
Stream configure message
Provider capture advertisement
Consumer’s fixed characteristics
Dynamic factors
e.g. number of screens
e.g. change of user preferences
simultaneous transmission set + encoding groups
Notes:   The idea is that the “receiver” (stream consumer) chooses from the set of media captures that the “sender” (stream producer) has advertised as being available.
    Receiver can factor in knowledge about its own configuration such as how many screens it has and what they are capable of
    Receiver must take account of sender constraints such as physical simultaneities and encoding group limitations
    Receiver must be prepared to rethink the streams it receives based on new information from the sender (for instance presentation streams may come and go as users connect and disconnect content sources e.g. laptops).

## Slide 6: Provider Capture Advertisement
Captures and attributes
Simultaneous transmission sets
Capture sets
Encoding groups
Notes: Shows different constituent elements of capture advertisement sent by provider

## Slide 7: Simultaneous Transmission Sets
Center camera can do either
regular or zoomed
People
Right
Center
VC1
VC2
Left
VC0
(VC0, VC1, VC2)
(VC0, VC3, VC2)
VC3
Notes: Simultaneous transmission sets allow sender to convey to the receiver which of its media capture streams can be sent at the same time
e.g. There might be restrictions here if the sender has to change physical cameras’ PTZ parameters to form different media captures
VC0, VC1 and VC2 can all be generated simultaneously whereas VC1 and VC3 cannot. VC0 + VC3 + VC2 not necessarily very useful, but not necessarily a need to forbid it
Ordering of captures within simultaneous sets not significant no spatial implication – “physical”

## Slide 8: Encoding Groups
Media Stream Provider
Encoding group
Encoding group
Encoding Group
Attribute Name | Description
maxBandwidth | Maximum number of bits per second relating to all encodes combined
maxVideoMbps | Maximum number of macroblocks per second relating to all video encodes combined: ((width + 15) / 16) * ((height + 15) / 16) * framesPerSecond
videoEncodes[] | Set of potential video encodes can be generated
audioEncodes[] | Set of potential audio encodes that can be generated
Notes:   Each media stream provider includes one or more encoding groups
  Unit of encoding capability
  Multiple encoding groups per system
  Some encoding systems are fixed, others flexible, e.g. single box with multiple DSPs
  Greatest efficiency is likely to be achieved by a device using a single encoding group for all of its encoding capability
    However, this would not always be possible for devices that comprise multiple separate physical boxes
  Encoding group has overall maxMbps and bandwidth limits, as well as comprising set of encodes
  A remote receiver (stream consumer) configures some or all of the specific encodings within one or more groups in order to provide it with media streams to decode

## Slide 9: Encoding Group Structure
Media stream provider
Encoding group
Encoding group
Encoding group
Encode 1
Encode 3
Encode 2
Notes:   More detail on Media stream provider’s encoding group structure
  Each encoding group has multiple potential actual encodings within it
  Not all encodings need to be equally capable – stream consumer chooses maximum characteristics of each when configuring it
  Typical 3 box system would have one encoding group per physical box

## Slide 10: Video Encode Attributes
Name | Description
maxBandwidth | Maximum number of bits per second relating to the video encode
maxMbps | Maximum number of macroblocks per second relating to the video encode: ((width + 15) / 16) * ((height + 15) / 16) * framesPerSecond
maxWidth | Video resolution’s maximum width, expressed in pixels
maxHeight | Video resolution’s maximum height, expressed in pixels
maxFrameRate | Maximum frame rate
Notes:   A remote receiver configures (i.e. instantiates) some or all of the specific encodes such that
      Config of each active ENC<n> does not exceed that encode’s maxWidth, maxHeight, maxFrameRate
      Total bandwidth of configured ENC<n> encodes does not exceed maxBandwidth of the encoding group
      Sum of macroblocks per second of each configured encode not exceed maxMbps attribute of the encoding group
    Equivalent set of attributes for audio encodes within an encoding group

## Slide 11: Sample Encoding Group
<=2 encodes, <= 1080p30
Bandwidth trade-off between encodes & group as a whole
EG0: maxMbps = 489600, maxBandwidth=6000000
  ENC0: maxWidth=1920, maxHeight=1080, maxFrameRate=60, maxMbps=244800, maxBandwidth=4000000
  ENC1: maxWidth=1920, maxHeight=1080, maxFrameRate=60, maxMbps=244800, maxBandwidth=4000000
Notes: “Simple” encoding group set up with no resolution / frame rate trade-off required - all encodings within the group can be maxed to 1080p30 and still fit within the maxMbps of the group)
bandwidth trade-off still needed (<= 4Meg for each encode but <= 6 Meg for each group)
3 box system would typically have 3 identical such encoding groups