## Slide 1: CLUE Legacy Mode
CLUE Design Team Meeting
1st October, 2013
Christer Holmberg

## Slide 2: ASSUMPTION
Even when communicating with a non-CLUE device, a CLUE device should be able to provide a good, high-quality, video experience.
  Must support the negotiating of critical information elements using SDP (or SIP), as CLUE cannot be used.

## Slide 3: Legacy SDP Offer from CLUE
When a CLUE entity sends an initial Offer for a session, or wishes to switch from a previously negotiated CLUE session to a legacy session, is MUST include at least the following media descriptions, and support the associated features:
  m = audio (main audio – legacy mode)
    Bi-directional
  m = video (main video – legacy mode)
    Bi-directional
    RTP/AVFP
    RTCP
    Full Intra Request (FIR), Codec-Control Messages (CCM)
    Temporary Maximum Media Bit-rate Request (TMMBR), Temporary Maximum Media Bit-rate Notification (TMMBN)
  m = video (presentation, screen sharing,…)
    a=content:slides
    Low frame rate & high resolution
  m = application (clue channel)
  NOTE: This does not prevent the CLUE entity from offering additional media, but a non-CLUE device that wants to communicate with a CLUE entity needs to be prepared to receive an Offer as described above (eventhough the non-CLUE entity does not need to accept all Offered media).

## Slide 4: CLUE-Legacy
CLUE
NON-CLUE
OFFER (Initial Legacy):
m=audio c_p1
m=video c_p2
m=video c_p3
m=application c_p4
ANSWER (Initial Legacy):
m=audio n_p1
m=video n_p2
m=video n_p3
m=application 0

## Slide 5: CLUE-CLUE
CLUE
CLUE
OFFER (Initial Legacy):
m=audio c_p1
m=video c_p2
m=video c_p3
m=application c_p4
ANSWER (Initial Legacy):
m=audio 0
m=video 0
m=video 0
m=application c_p4
OFFER (CLUE):
m=audio 0
m=video 0
m=video 0
m=application c_p4
m=audio_clue c_p5
m=audio_clue c_p6
m=video_clue c_p7
m=video_clue c_p8
CLUE Exchange

## Slide 6: CLUE-CLUE FALLBACK TO LEGACY
CLUE
CLUE
OFFER (Back to Legacy):
m=audio c_p1
m=video c_p2
m=video c_p3
m=application 0
m=audio_clue 0
m=audio_clue 0
m=video_clue 0
m=video_clue 0
ANSWER (Back to Legacy):
m=audio c_p1
m=video c_p1
m=video c_p1
m=application 0
m=audio_clue 0
m=audio_clue 0
m=video_clue 0
m=video_clue 0
CLUE SESSION