## Slide 1: MPTCP Implementation: Use cases for Enhancement Opportunities
A.Palanivelan Chetan Harsha Senthil Sivakumar
(palanivelan.appanasamy@intl.verizon.com) (chetan.harsha@intl.verizon.com) (ssenthil@cisco.com)
IETF-93 MPTCP WG

## Slide 2: Introduction
The Intention of this proposal is to document Opportunities, where Enhancements to MPTCP can translate to more wider deployments
The Scope of the use cases/problem statement(s) discussed is limited to impact on enduser experience only

## Slide 3: What is this about?
Document use cases (Draft-01)
Prioritize use cases (WG discussion)
Design recommendations/solutions (new draft?)

## Slide 4: Use cases
Short Flows vs Long Flows:
Too many Small Flows => Higher Number of Transactions. But, much less Bandwidth Consumption
Far Lesser Long Flows => Lesser Number of Transactions. But, higher Bandwidth Consumption

## Slide 5: Use cases
Too many Small Flows => Higher Number of Transactions. But much less Bandwidth Consumption
  Can we achieve Low latency for short flows?
    Average completion of flow with mptcp can be higher than completion time without mptcp
    With Bunch of Short Flows, MPTCP may negatively impact throughput
    Even a single lost packet can force an entire connection to wait for an RTO.
Far Less Long Flows => Lesser Number of Transactions, But Higher Bandwidth Consumption
  Can we achieve higher Throughput for Long Flows?
    Without compromising on performance
  How do we maintain Reliability?
    How do we manage tolerance to sudden and high bursts of traffic?
Both long and short flows are important from the enduser perspective. We need to come up with appropriate definition and clear demarcation for short and long flows, from MPTCP Perspective. These need be dealt differently (Probably with multiple profiles).
Notes:   Throughput/Performance
http://conferences.sigcomm.org/sigcomm/2015/pdf/papers/p349.pdf
The existing profiles cannot scale for all type of applications in MPTCP context, hence there is a need to have different profiles/mechanisms based on the applications like short videos, long videos etc.
  Window size, adaptive buffering
The current window sizing and buffering mechanisms are designed to be suited for TCP flows, hence on moving to MPTCP scenarios the way of setting these TCP parameters impacts the applications.
  Custom Optimization Techniques
The existing optimization either in data center or enterprise applications are designed for handling specific deployments. Thus MPTCP when enabled on these applications should not deteriorate the current performance.

## Slide 6: Use cases
Application based Path selection and Adaptive buffering:
Elastic vs Inelastic Applications
  Different way of handling packets => Better Performance.
MPTCP performance is impacted …
  When the size of the receive buffer is limited.
  Path with high RTT may result in the receive buffer size growing beyond the allowed maximum
  Diversified RTT
Application based Path Selection and Adaptive Buffering can help with the above scenarios. Tweaking the buffer sizes based on the type of application and/or network condition can positively impact the flows.
Notes: RTT Impact:
  The concern with using paths of different RTTs is not limited to the effect on the size of the receive buffer. Although MPTCP’s joint congestion control makes sure that the paths of higher RTT are used less often than those with lower RTT, it maintains a minimum rate of transmission on these paths in order to probe for any changes in path characteristics. This behavior may greatly impact MPTCP performance as the application would have to wait for the missing segments before it can read from the receive buffer

## Slide 7: Use cases
Path Selection Enhancements?
Usecases where MPTCP path selection can be enhanced:
  For High packet loss and High latency networks?
  Multiple profiles to dynamically switch (move across) the networks?
  Roaming scenarios
The best optimal path is ever changing in Internet. Frequent switching may cause unnecessary overheads and can impact performance. Enhanced yet controlled Path Selection and Path Switching can help get better performance out of the network.

## Slide 8: Use cases
Optimal number of paths:
Controlling the number of subflows getting created…
  How many is too many?
  Can this be controlled? What Inputs to Consider?
    Based on Network Characteristics
    Historic data (region wise)

## Slide 9: More Use cases
Security
  Address Correlation
  Potential phishing attacks

## Slide 10
THANK YOU